## Slide 1: Tutorial for UBEM District Description
Created by Royden Soh Wei Jun, 11 June 2025

## Slide 2: Prerequisites
Basic Rhino3D understanding
Basic Grasshopper understanding
Anemone module downloaded for Grasshopper
  Version: Anemone 0.4
  https://www.food4rhino.com/en/app/anemone

## Slide 3: Overall Workflow
Create (or get existing) district massing
Assign an archetype to each building
Use custom Grasshopper script to calculate GFA of each building
Copy data to excel sheet (District Individual Building GFAs.xlsx)
Run EC_district Python scripts

## Slide 4: 1) Create/Get district massing

## Slide 5
1) Create/Get district massing
If you already have the massing of the district you want to study, great! Go to step 2.
Some cases for this include:
  An existing (already constructed) district
  Confirmed plans for an upcoming district
Otherwise…

## Slide 6
1) Create/Get district massing
If you need to create a plausible district massing, here are some guidelines for the Singapore context:
Get the latest Master Plan from https://eservice.ura.gov.sg/maps/?service=MP. Screenshot, import into Rhino, and ensure the image is scaled appropriately to reflect real world dimensions.
Ensure proper scaling in Rhino by including the Master Plan scale in the screenshot

## Slide 7
1) Create/Get district massing
If analysing an upcoming district, check the URA website to see if any GFA guidelines or regulations are released. These are constraints that must be followed.
(example: Technical Conditions of Tender for Jurong Lake District)
District-wide GFA restrictions
Office GFA restrictions

## Slide 8
1) Create/Get district massing
If analysing an upcoming district, check the URA website to see if any GFA guidelines or regulations are released. These are constraints that must be followed.
Residential GFA restrictions
(example: Technical Conditions of Tender for Jurong Lake District)

## Slide 9
1) Create/Get district massing
Create a more realistic massing by using https://cadmapper.com/ and copying existing building massing to the study area
Copy existing massing to study area

## Slide 10: 2) Assign an archetype to each building

## Slide 11
2) Assign an archetype to each building
In Rhino, create a layer or sub-layer for each building archetype
(example: Jurong Lake District where we suppose that these 5 archetypes will make up the entire district)

## Slide 12
2) Assign an archetype to each building
For each building, assign it to the correct layer
Use the “ChangeLayer” command in Rhino

## Slide 13: 3) Use custom Grasshopper script to calculate GFA of each building

## Slide 14
3) Use custom Grasshopper script to calculate GFA of each building
Open the Grasshopper file: Building GFA Calculator.gh
This “All Archetypes” part represents a copy-able module

## Slide 15
3) Use custom Grasshopper script to calculate GFA of each building
3 main inputs to the module are required:
  The ground plane
  The Breps for the appropriate building massing
  The floor to floor height
1) Ground plane
2) Archetype Breps
3) Floor to floor height

## Slide 16
3) Use custom Grasshopper script to calculate GFA of each building
Input 1: ground plane
  Simply create a plane at z = 0 using the Rhino “Plane” command
  Thus, this script assumes that the district is sitting on flat ground (unable to deal with uneven terrain)

## Slide 17
3) Use custom Grasshopper script to calculate GFA of each building
Input 1: ground plane
  In Grasshopper, right click on the Surface component > Set one Surface
  Then click on the created plane in Rhino to select it

## Slide 18
3) Use custom Grasshopper script to calculate GFA of each building
Input 2: archetype Breps
  In Grasshopper, right click on the Brep component > Set Multiple Breps

## Slide 19
3) Use custom Grasshopper script to calculate GFA of each building
Input 2: archetype Breps
  In Rhino, select all the buildings that belong to the archetype being studied
  In this case, the module is for “All Archetypes” so in this case with the Rhino layers structured in this manner, we
    Right-click on Proposed Massing
    Click on Select Sublayer Objects
    Press Enter

## Slide 20
3) Use custom Grasshopper script to calculate GFA of each building
Input 2: archetype Breps
  If for example, you only want to get the GFAs of buildings belonging to the Retail archetype,
  Right click on the Retail layer
  Click on Select Objects
  Press Enter

## Slide 21
3) Use custom Grasshopper script to calculate GFA of each building
Now numbers might appear, but we need to make sure that the calculation loop executes properly
Click the button to start the execution of the GFA calculation loop
Loop button

## Slide 22
3) Use custom Grasshopper script to calculate GFA of each building
Now we look at the right side of the Grasshopper module where the GFA results have been calculated
Results area

## Slide 23
3) Use custom Grasshopper script to calculate GFA of each building
Due to some funny way that Grasshopper operates, a null value will be introduced into the list under “CFA total for each building”
In this case, it appears at #55 (will be different for each case)
Null value (in this case, at #55)

## Slide 24
3) Use custom Grasshopper script to calculate GFA of each building
We need to manually resolve this by stating the correct serial number to replace with a zero
In this case, we use 55.
Change the serial number (in this case, to 55)

## Slide 25
3) Use custom Grasshopper script to calculate GFA of each building
A list of only numbers will then be generated, representing the CFA of every building, individually
List of individual building CFAs

## Slide 26
3) Use custom Grasshopper script to calculate GFA of each building
Sanity check, the CFA total across all the selected buildings should match
CFA total should match

## Slide 27
3) Use custom Grasshopper script to calculate GFA of each building
So in summary, we now have, for all the selected buildings in this module:
  The total CFA across all the buildings
  The list of individual building CFAs
2) List of individual building CFAs
1) Total CFA across all buildings

## Slide 28: 3.5) Using the Grasshopper script on each archetype

## Slide 29
3.5) Using the Grasshopper script on each archetype
The example shown in Step 3 was for “All Archetypes”
To do it for each archetype separately, simply copy and paste the module
Copy and paste the module somewhere else in the Grasshopper script

## Slide 30
3.5) Using the Grasshopper script on each archetype
Change the module label so you don’t get confused

## Slide 31
3.5) Using the Grasshopper script on each archetype
The ground plane is assumed to be the same, and hence no change is needed
You only need to change:
  select only the appropriate Breps (in this case, HDB Breps)
  The floor to floor height

## Slide 32: 4) Copy data to excel sheet

## Slide 33
4) Copy data to excel sheet
Copy the individual building CFAs by right clicking on the list > Copy Data Only

## Slide 34
4) Copy data to excel sheet
Open data/District Individual Building GFAs.xlsx

## Slide 35
4) Copy data to excel sheet
Paste the data under the “Individual Building GFA” column

## Slide 36
4) Copy data to excel sheet
In this case, the GFAs were copied from a module in the Grasshopper script dealing with only HDB buildings
Hence, we fill in “HDB” under the “Archetype” column

## Slide 37
4) Copy data to excel sheet
Feel free to delete the entry where the GFA = 0
For the case of embodied carbon only, this is not necessary but it is still good practice to do so
Delete GFA = 0 entry!

## Slide 38
4) Copy data to excel sheet
Copy in the rest of the archetypes until you have a complete description of the district being studied
Remember to delete GFA = 0 entries

## Slide 39: 5) Run EC_district Python scripts

## Slide 40
5) Run EC_district Python scripts
This consists of 2 scripts in the src folder:
  EC_district_execution.py
  EC_district_results.py
Follow the Python_Documentation.md file for more detailed instructions on how to use these scripts.